## Slide 1
CTTC NETWORK ONTOLOGY · WORKING MODEL v0.1
A graph of the network,
not another database.
CTTC's topology can be represented as an ontology, and the assessment materials already contain enough structure to seed one. The ontology is the missing piece between “the data exists in nine systems” and “the AI layer can explain what just happened.”
Every use case in the discussion brief resolves to a graph traversal — related alarms share an ancestor, customer impact is a walk from a port to its services, blast radius is a node removed and reachability recomputed.
FIVE LAYERS, EACH BINDING TO THE ONE BELOW
L4
Inferred
Fault domains · blast radius · risk findings
L3
Operational
Alarms · tickets · changes · versions · defects
L2
Service
Services · ordered paths · subscribers · SLAs
L1
Logical
PON trees · EVPN · VRFs · the ERPS ring
L0
Physical
Sites · chassis · ports · optics · fibre · ONTs
Build order is forced: no blast radius without service paths, no service paths without ports and adjacencies.
Ontology model
Five layers, a fifteen-class spine, class reference, and the seven decisions that are expensive to reverse.
Graph schema
22 labels, 18 relationship types, constraints, and six Cypher queries that answer real CTTC questions.
Loader + explorer
Python loader for Neo4j and a self-contained interactive topology view of the whole network.
San Angelo scope
Six-week bounded proof of value on one aggregation path, with a real decision gate.
Notes: Opening frame: this is not a modelling nicety layered on top of the AI concept — it is the concept. Every use case in the discussion brief is a graph traversal, and without a shared representation of what a device, port, PON, path, service and subscriber are, a language model is left inferring topology from alarm text. Four deliverables exist today: the model, the implementable schema, working code, and a bounded scope for proving it.

## Slide 2
WHAT IT SURFACES
Questions that take an engineer an afternoon become one traversal.
3
devices off their model's release
The San Angelo MX304 on 22.3R3, and two ACX units two trains back on 21.4R3 — from inventory data alone.
8
devices on defect-affected software
The release San Angelo was downgraded away from is still running everywhere else. Nobody spots that in a spreadsheet.
28
ONTs narrowed to one uplink
A four-minute alarm cluster bounded to the OLT uplink — using three negative-evidence checks, not a guess.
3
services off their intended path
Up, billing normally, riding an unprotected route. No alarm fires for this condition today.
Demonstrated on a dataset built from the assessment's real models, counts and releases; identifiers below device level are placeholders.
NEXT STEP
San Angelo, end to end
Six weeks. Build L0–L2 for one aggregation path — deep enough to walk an engineer from a subscriber to a defect and back.
Chosen because it already holds two documented anomalies and exercises both vendors.
BEFORE ANYTHING STARTS
Currency check.
All of this is built from the 18 May review. Confirm the anomalies still hold.
Identity precedence.
Which system wins per property when inventory, NMS, GIS and ticketing disagree. A CTTC decision — and nothing loads until it is made.
Innosquares · companion pages: ontology model, graph schema, network explorer, San Angelo scope
Notes: Lead with the fourth stat, not the first: services off their intended path is the one that surfaces a class of risk nothing in the current toolset reports. The first three make existing work faster; that one shows something new. Be explicit that the numbers come from a demo dataset — real models, counts and releases from the assessment, placeholder identifiers below device level. Close on the two blockers: the assessment is three months old, and identity-resolution precedence is a CTTC decision that gates every load.